## Slide 1: An open-source framework for the quantification of Urban Heat Islands based on Swiss open-data
Presenter: Zetong Liu
Supervised by Jerome Kaempf

## Slide 2: Work Objectives
1. Build an open-source framework in Python to go from Swiss open-datasets to indicators related to the Urban Heat Island effect
2. Demonstrate the application of scenarios on one case-study representative of the Swiss landscape, quantifying improvement measures

## Slide 3: Previous Work
Olivier Chavanne's master thesis
A python workflow was built:
1, Process and analyze information of all buildings in the area of his study
2, Simulate the surface temperature of those buildings through Citysim.
To measuring the effect of UHI, the effect of different kinds of grounds, e.g. asphalt road, concrete road, green areas, around buildings need to be added.

## Slide 4: Identification of necessary open-data
swissBUILDINGS3D 3.0 Beta -> Buildings as 3D models
geodienste.ch, official survey -> geometric footprints of buildings
swissALTI3D -> coordinates of grounds
swissTLM3D -> roads and green ground
IDAWEB and Meteonorm-> climate data

## Slide 5
SwissALT 3D
Official Survey, layer lcsf filtered by genre=‘batiment’
Visualisation of Swiss open datasets in QGIS
SwissBuildings3D, layers roof, wall and floor
SwissTLM 3D, layers tlm_bb_bodenbedeckung and
tlm_strassen_strasse

## Slide 6: Defined composites of grounds
kFactor represents humidity of the material
the ability to reflect solar energy

## Slide 7: Code work
def add_ground_from_XYZ(MO_dhn, district, terrain_df, zone_box, center_coordinates=(0,0), kFactor, groundtype, detailedSimulation=False, ShortWaveReflectance)
  Create mesh of ground
  Discard grounds under buildings:
    Create a box around zone_tout
    Only keep triangle surfaces that are in the box and not intersects with any buildings in zone_cad
  Create a geodataframe that contains all triangles objects and assign all grounds the type of concrete road
FINAL PRESENTATION
v1
v2
v4
v3

## Slide 8: Code work
def modify_type(district, ground_data, green_data, street_data, green_groundtype, road_groundtype, green_kfactor, green_SWR, road_kfactor, road_SWR) #
  Find grounds of road and green area through intersection with streets and green area objects
  Modify the type of original ground to a new type of road ground(concrete, asphalt or permeable pavement) or green area and attach physical characteristics like kFactor and short wave reflectance accordingly
    Buffer street from line objects to polygon objects
    Find the list of triangles that intersect with buffered streets, then modify corresponding triangles
    Do the same for green areas
FINAL PRESENTATION

## Slide 9
Green area simulated by coarse ground mesh
Green area simulated by fine ground mesh
Example of simulation with different resolution of ground mesh

## Slide 10
Roads simulated by ground mesh (resolution=2m)
Roads simulated by fine ground mesh(resolution=0.5m)
Example of simulation with different resolution of ground mesh

## Slide 11: Code work
def cut(district, ground_data, MO_dhn, footprints, kept_range=15)
  Create a buffer of 15 meters around each buildings within my study area of interest
  Only keep grounds within the convex hull of those buffered buildings
  Only keep buildings that intersect or are within convex hull of those buffered buildings
  Reasons:
  1, Distant buildings and roads have little thermal impact on my study area of interest.
  2, Save computational time.
FINAL PRESENTATION

## Slide 12: Code work
def AST(envelope, Temp, ground_data)
  Calculate average surface temperature of each building as and atribute them to corresponding building according to surface_id
  Attribute temperature of each ground triangle according to gid
Assume that a building contains n surfaces with temperature on surface . The area of surface is , average surface(wall and roof surfaces) temperature is .
This map the temperature information on 3D objects to 2D objects to be shown in QGIS
FINAL PRESENTATION

## Slide 13: Workflow
Streets
Scenario1
FINAL PRESENTATION
Zone_cad
Zone_tout
XYZ
Xml(default ground)
Temperature(_TS.out)
Wall
Floor
roof
Surface_with_temperature
Envelope
Streets
Green areas
Simulate-Citysim
add_ground_from_XYZ
Xml(ground modified)
modify_type
AST
cut
Xml(distant objects cut)
Xml_root
Climate

## Slide 14: Case Study – Fontaine de la Justice, Lausanne
Motivation: It’s important to keep small roads cool in old town center

## Slide 15: CitySim Pro Visualization
Top view
Bottom view
3D view

## Slide 16
Scenario 1: replace some city roads with green area

## Slide 17
Before adding green area
After adding green area
Temperature classification(Celsius degree)

## Slide 18
Scenario 1: replace some city roads with green area
A samller sample of current case: Contemporary yearly average surface temperature
Colorful buidings = buildings of interest
Dark buildings = buidlgins just to cast shades
Streets is colder due to shadows and green areas

## Slide 19
Contemporary
2040
Climate change
2030
Evident temprerature increment

## Slide 20: Decreased Temperature w.r.t climate change
2030
2040
Contemporary
[-1.81, 0]
range
[-1.9, 0]
[-1.93, 0]
Weighted average
-0.02297
-0.02400
-0.02431
Effects of cooling brought by green areas prevail

## Slide 21: Conclusions
Obtained open-data for grounds and visualised them in QGIS
Finalised the mesh of grounds
Obtained open-data for green area and roads, and attributed right physical characteristics
Run the case of Lausanne and visualised the results in CitySim Pro
Gather Meteorological data for now, 2030, 2040, 2050
Run case-study with meteorological data and visualise reseults in QGIS
Demonstrate one scenario with original grounds replaced by green grounds and visualized their effects on urban heat islands in QGIS
Identified that decreased temperature around green area is perceptible.
Github: https://github.com/ZetongLiu/UHI_CH_sp

## Slide 22: Prospects
Develop an algorithm that can create adaptive mesh of grounds, i.e. finer mesh at sharp part of geometry objects.Run case-study with trees and showcase their effects on UHI
Attach the exact types of street in reality to each street data and change ground type accordingly.
Add trees into our framework and study their effects on UHI
Add water into our framework and study their effects on UHI

## Slide 23: References
https://github.com/ochavanne/CAD-O
Upadhyay, G ; Kämpf, J; Scartezzini, J: Ground temperature modeling: The case study of Rue des Maraîchers in Geneva, 2014, URL: https://infoscience.epfl.ch/record/198754?ln=fr
https://github.com/kaemco/CitySim-Solver/wiki/The-district#groundsurface
https://www.eoas.ubc.ca/courses/eosc350/content/foundations/properties/density.htm#:~:text=Remarks,2.6%20and%202.7g%2Fcc.
https://www.bruk.info.pl/en/guide/stone-size-thickness-and-chamfer-should-technical-parameters-matter-to-us/
https://www.sciencedirect.com/science/article/pii/S2214509518300482#sec0010
FINAL PRESENTATION